## Slide 1: VITISH 2026 (SIH Internal Hackathon)
The design file already knows what should be on the board.
Problem Statement ID: VITISH-82
Problem Statement Title: Low-cost Optical Inspection for PCB Assembly
Theme: Smart Automation / Manufacturing
PS Category: Hardware
Idea Title: GerberEye — CAD-Referenced Optical Inspection
Team Name: <team name>
Team ID: <team id>
154
unit tests passing
29/29
integration checks
0
network calls made
Commercial AOI: ₹15–50 lakh. This: under ₹10,000, on the laptop the shop already owns.

## Slide 2: IDEA TITLE — GerberEye: CAD-Referenced PCB Inspection
THE PROBLEM
▸ An MSME inspects assembled PCBs by eye, under a magnifier lamp
▸ ~200 reference designators cross-checked against a printed drawing
▸ Accuracy falls with fatigue and board density; nothing is recorded
▸ Automating it costs ₹15–50 lakh — more than the shop earns in a year
THE INSIGHT
▸ The shop already owns the design files — it cannot manufacture without them
▸ The pick-and-place file states what sits at every coordinate
▸ So: the design file is the label
▸ No training data. No annotation. No dataset needed.
HOW IT WORKS
Design files
Gerber · P&P · BOM
Register
CAD → camera
Extract ROI
per component
Classify
absent/rotated/offset
Verdict
pass / fail
Record
CSV · trends
INNOVATION & UNIQUENESS
 | Conventional approach | GerberEye
Reference | Operator memory / printed drawing | The CAD file itself
Training data | Thousands of labelled defect images | None — the P&P file is the label
Output | "This board looks wrong" | "U1 rotated 90°, C2 missing"
Cost / connectivity | ₹15–50 lakh, vendor-tied | < ₹10,000, fully offline

## Slide 3: TECHNICAL APPROACH
INSPECTION PIPELINE — CPU only, no GPU, ~100 ms per board
Capture
locked exposure
Detect markers
ArUco / fiducial
Homography
mm → pixels
Project parts
footprint extents
Template match
~2 ms/part
Verdict
IPC-A-610 classes
Persist
append-only
TWO-PATH ARCHITECTURE (ADR-002)
Path | Needs | Gives
A — Golden differencing | One known-good board | Regions that differ
B — CAD registration | Gerber + pick-and-place | Defects named by designator
Path A works with zero design files, so the demo cannot be blocked by a missing CAD↔board pair. Path B is the differentiator.
TECHNOLOGY STACK — permissive licences only
Layer | Choice | Licence
Computer vision | OpenCV | Apache-2.0
CAD parsing | pygerber | MIT
Backend | Python · FastAPI · SQLite | MIT
Operator UI | React + Vite | MIT
Compute | Laptop CPU / Raspberry Pi | —
Why not YOLO / deep learning? The latency budget allows ~6 ms per component on a CPU with no GPU — and Ultralytics is AGPL-3.0, so an MSME deploying it would inherit a copyleft obligation. Every dependency here is MIT, Apache-2.0 or BSD.
The hard part is registration, not comparison. CAD is in millimetres about a board datum; the camera sees pixels at unknown scale and perspective. Solving that homography is what makes "is C2 present?" answerable — and it needs Gerber knowledge and computer vision.

## Slide 4: SOLUTION FEASIBILITY & VIABILITY
ALREADY BUILT AND VERIFIED
Capability | Evidence
Full pipeline, end to end | 154 unit tests, 0 failing
Frontend ↔ backend wiring | 29 / 29 integration checks
Defect naming + classification | absent / rotated / offset + measurement
Audit trail | append-only records, CSV export
Runs with no camera at all | demo mode + simulated bench
INDICATIVE BILL OF MATERIALS
Item | Cost
USB webcam, 1080p | ₹1,200
LED ring light + diffuser | ₹900
Fixed jig, mount, enclosure | ₹1,600
Raspberry Pi (optional edge node) | ₹4,800
Laptop | already owned
Total | < ₹10,000
RISKS AND HOW EACH IS CONTAINED
Risk | Why it matters | Containment
Illumination instability | Dominant term in the false-call rate — larger than any algorithm change | Stability gate refuses to trust thresholds above 2 grey levels; degraded state shown, not hidden
Camera refuses exposure lock | Breaks golden-board comparison between captures | Detected and reported; enclosure controls ambient light; reproduced in simulation for testing
No matched CAD ↔ board pair yet | Path B cannot be demonstrated on that board | Two-path design — Path A needs no design files at all
Hardware failure on demo day | Loses the live demonstration | Demo mode is a complete working station with no camera attached
Stated honestly: recall and false-call rate are not yet measured — that needs seeded defects on real boards. We offer falsifiability instead: hand us a board, pull a component, and we will re-run it in front of you.
mimo v2.5 vs dee

## Slide 5: REAL WORLD IMPACTS, BENEFITS & RELEVANCE
WHAT CHANGES ON THE SHOP FLOOR
 | Today | With GerberEye
Method | Eye + magnifier + printed assembly drawing | Camera + the shop's own design files
Time per board | 2–5 minutes of concentrated attention | Seconds, unattended
What the operator is told | "Something looks wrong here" | "U1 rotated 90°. C2 missing. R5 off its pads by 1.6 mm"
Record of inspection | A signature on a sheet | Machine-generated record, exportable as CSV
Cost to automate | ₹15–50 lakh | Under ₹10,000
ECONOMIC
▸ Defects caught in-house, not at the customer's incoming inspection
▸ An inspection trail lets an MSME bid for contracts that require one
▸ Recurring-defect trends turn detection into process improvement — a feeder fault, not a rework job
SOCIAL
▸ The operator is always the authority — one-click override, no form to fill
▸ Augments the inspector rather than replacing them; no de-skilling
▸ Removes the fatigue-driven error that eye inspection makes inevitable
STRATEGIC
▸ Frugal Industry 4.0 for MSMEs — aligned with SAMARTH Udyog Bharat 4.0
▸ Zero network egress — customer design IP never leaves the machine
▸ Built to IPC-A-610 defect taxonomy; IPC-2591 (CFX) ready for MES integration
CAD software checks whether the design is correct. GerberEye checks whether the board in your hand matches it. Design defects happen once; assembly defects happen on every unit, on every shift.

## Slide 6: TEAM CAPABILITY
TEAM AND ROLES — 5 CSE + 1 ECE
Stream | Ownership
Capture & golden reference | ECE — jig, lighting, camera settings
Differencing engine (Path A) | CSE — computer vision
CAD registration (Path B) | CSE — Gerber / pick-and-place, homography
Backend & data | CSE — FastAPI, SQLite, records
Operator UI | CSE — React, overlay, override
Demo, risk & pitch | Team lead
PROOF OF WORK — this repository
Artefact | Scale
Requirements engineering | 27 functional, 13 non-functional, 16 stakeholder
Architecture | 6 ADRs, C4 model, ATAM-lite evaluation
Implementation | ~7,800 lines; 154 tests; 29 integration checks
Traceability | Every requirement traced both directions, orphan-checked
Working prototype | Runs end to end today, with no hardware
WHY THIS DOMAIN — AND WHAT WE FOUND IN OUR OWN SYSTEM
We benchmarked against a 221-component 0603 board rather than our own demo board. Two of five seeded defects were missed — both of them 'missing components', the class that should be easiest. A removed 0603 changes ~100 px² of contour area; the default noise floor was 120 px², so the region was discarded and the board reported PASS.
That is an escape, not a false call — the dangerous direction. The station now computes the smallest component's expected change from its footprint and warns when the threshold would hide it.
Finding a silent recall failure in your own system, and building the guard that surfaces it, is the capability we would most like to be judged on.

## Slide 7: RESEARCH AND REFERENCES
STANDARDS AND SPECIFICATIONS
Reference | What it gives the project
IPC-A-610 — Acceptability of Electronic Assemblies | The defect taxonomy: absent, misaligned, rotated, polarity-reversed, tombstoned
IPC-2591 (CFX) — Connected Factory Exchange | The MES integration path — how an inspection station reports to a factory line
Gerber RS-274X / X2 (Ucamco specification) | Board geometry; X2 attributes carry component and net metadata
Pick-and-place / centroid file (CAD output) | Reference designator, X, Y, rotation, side — the ground truth used as the label
LIBRARIES AND TECHNIQUES
▸ OpenCV — ArUco marker detection, homography (RANSAC), ECC alignment, template matching
▸ pygerber — Gerber rendering to raster for CAD-to-camera reference
▸ Golden-board differencing — the classical AOI baseline, used as the no-design-files path
▸ Surveyed PatchCore / anomalib few-shot anomaly detection — deferred: CPU latency budget
FINDINGS THAT SHAPED THE DESIGN
▸ Public PCB datasets (DeepPCB, HRIPCB) are bare-board trace defects — the wrong problem entirely
▸ No usable public dataset of PCB assembly defects exists → so the design file must be the label
▸ GitHub survey: no prior art for projecting Gerber/pick-and-place onto a live camera frame
▸ Commercial AOI is vendor-locked and cloud-tied — offline operation is a requirement, not a feature
Working prototype, requirements set and architecture decision records: github.com/Haise-727/pcb-catcher